## Slide 1: Binary Arithmetic and Boolean Operators

## Slide 2: Base 10 addition
How do you add two multi-digit numbers in base 10?
  Line up the numbers on the right
  Add the digits in the rightmost column
  If the resulting sum has 2 digits, carry over the tens digit to the next column on the left
  Repeat for all columns, working from right to left

## Slide 3: Base 10 addition
1
1 0 2 4
+ 7 6 8
---------
1 7 9 2
4 + 8 = 12 Write 2 in the sum, carry 1
1 + 2 + 6 = 9 Write 9 in the sum, no carry
0 + 7 = 7 Write 7 in the sum, no carry
1 + 0 = 1 Write 1 in the sum, no carry
1
2
3
4

## Slide 4: Base 2 addition
This process works exactly the same in base 2, but the arithmetic is done in base 2
1 1
1 1 1 0
+ 1 1 1
----------
1 0 1 0 1
0 + 1 = 1 Write 1 in the sum, no carry
1 + 1 = 10 Write 0 in the sum, carry 1
1 + 1 + 1 = 11 Write 1 in the sum, carry 1
1 + 1 = 10 No more columns to carry to, so just write 10 in the sum
1
2
3
4

## Slide 5: Computers and base 2 addition
Remember that a computer represents everything (including numbers) using sequences of bits (0’s and 1’s)
How does a computer perform addition on two binary numbers?
To answer this, we first need to discuss the concept of Boolean operators

## Slide 6: Operators and operands
First, a bit of terminology!
Think of a simple math expression like 2 + 3
  The numbers 2 and 3 are known as operands
  The + is an operator: it specifies what action to perform on the operands
  The result of the expression is another number (in this case, the number 5)

## Slide 7: Boolean operators
When we talk about Boolean operators, we’re referring to operations that are carried out on individual bits instead of base 10 numbers
Three Boolean operators we'll discuss: AND, OR, NOT
We can use these Boolean operators to write Boolean expressions, such as 1 OR 0
  Here the 1 and 0 are the operands
  The OR is the operator
  The result of the expression is another bit (it turns out to be 1 here)
You need to memorize the definitions of AND, OR, NOT – we will use them again throughout the course!

## Slide 8: The AND operator
Given any two bits A and B: A AND B yields 1 if both A and B are 1, 0 otherwise
Often written as A && B
Examples: 1 && 0 results in 0 1 && 1 results in 1 0 && 0 results in 0

## Slide 9: The OR operator
Given any two bits A and B: A OR B yields 1 if at least one of A and B is 1, 0 otherwise
Often written as A || B
Examples: 1 || 0 results in 1 1 || 1 results in 1 0 || 0 results in 0

## Slide 10: The NOT operator
Given any one bit A: NOT A yields the opposite of A
Often written as !A
Examples: !1 results in 0 !0 results in 1

## Slide 11: Boolean expressions
In ordinary arithmetic, we can use the four basic operators (+, -, *, /) to combine numbers (operands) into long expressions
  Example: (6 + 5) * 9 / (3 + 10)
Similarly, we can use Boolean operators (&&, ||, !) to combine bits (operands) into long Boolean expressions
  Example: (1 || 0) && (!0 && !(1 || 0))

## Slide 12: Evaluating Boolean expressions
To properly evaluate (find the value or result of) a Boolean expression, the operations need to be done in a certain order
In ordinary arithmetic (PEMDAS):
  Parentheses (innermost first)
  Exponents
  Multiplication / Division (from left to right)
  Addition / Subtraction (from left to right)
In Boolean expressions:
  Parentheses (innermost first)
  NOT
  AND
  OR

## Slide 13: Evaluating Boolean expressions
Example: Evaluate the Boolean expression 0 && !1 || !0 && 1
  First, handle the NOT operators: 0 && !1 || !0 && 1 = 0 && 0 || 1 && 1
  Then do AND: 0 && 0 || 1 && 1 = 0 || 1
  Then do OR: 0 || 1 = 1
Final answer

## Slide 14: Truth tables
A truth table lists the result of a Boolean expression for all possible combinations of its operands
If we have two operands, then there are four possible combinations:
  Both operands are 0
  The first operand is 0, the second is 1
  The first operand is 1, the second is 0
  Both operands are 1
More generally: Each operand is 1 bit (2 possible values), so a truth table for a Boolean expression with n operands needs to consider 2n total possibilities

## Slide 15: Truth table for the AND operator
A | B | A && B
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
“When A = 0 and B = 0, A && B = 0”
“When A = 0 and B = 1, A && B = 0”
“When A = 1 and B = 0, A && B = 0”
“When A = 1 and B = 1, A && B = 1”
Operands
Result
AND involves two operands, so the truth table must consider 22 possibilities.

## Slide 16: Truth tables for OR, NOT
A | !A
0 | 1
1 | 0
OR involves two operands, so the truth table must consider 22 possibilities.
NOT involves only one operand, so the truth table needs to consider only 21 possibilities.
A | B | A ¦¦ B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1